## Slide 1: ETHERNET

## Slide 2: CATEGORY 1
Category 1 (Cat 1) cable is an early form of unshielded twisted pair (UTP) wiring, primarily designed for analogue voice communication. It was widely used in telephone systems, commonly referred to as Plain Old Telephone Service (POTS), before the 1980s
2 strands

## Slide 3: CATEGORY 2
Category 2 (Cat 2) cable is an early form of unshielded twisted pair (UTP) cabling that was primarily used in the 1980s and early 1990s for both telephone and low-speed data communications. It served as a transitional solution between voice-only Cat 1 cabling and the more advanced data-capable cables that followed.
4 strands

## Slide 4: CATEGORY 3
Category 3 (Cat 3) cable is an unshielded twisted pair (UTP) cable that was widely used in the early 1990s for telephone and data communications. It was commonly employed in early Ethernet networks, supporting data rates of up to 10 Mbps over distances of up to 100 meters.
6 strands

## Slide 5: CATEGORY 4
Category 4 (Cat 4) cable is an unshielded twisted pair (UTP) cabling standard that was used primarily in the late 1980s and early 1990s for voice and data transmission. It offered improved performance over its predecessor, Cat 3, but was quickly superseded by higher-category cables.FEDUS
8 strands

## Slide 6: CATEGORY 5
Category 5 (Cat 5) cable is a type of unshielded twisted pair (UTP) cabling that was widely used in the late 1990s and early 2000s for Ethernet and telephone networks. It was designed to support data transmission speeds of up to 100 Mbps over distances up to 100 meters.
Too much in Telopea park school
Its shit.
8 strands

## Slide 7: CATEGORY 5E
Category 5e (Cat 5e) cable is an enhanced version of the original Category 5 (Cat 5) Ethernet cable, designed to support higher data transmission speeds and reduce interference. It has become a standard choice for many networking applications due to its balance of performance and cost-effectiveness.
8 strands
Separator

## Slide 8: CATEGORY 6
Category 6 (Cat 6) cable is a standardized twisted pair cable designed for Ethernet and other network physical layers. It offers enhanced performance over its predecessors, making it suitable for high-speed and high-bandwidth applications.
8 strands
Separator

## Slide 9: CATEGORY 6A
Category 6A (Cat 6A) is an advanced twisted-pair Ethernet cable standard designed to support high-speed networking applications. It offers significant improvements over its predecessor, Cat 6, particularly in terms of data transmission rates and distance capabilities.
8 strands
Separator
Grounding Sheild

## Slide 10: CATEGORY 7
Cat 7, or Category 7, is a type of twisted pair cable used in networking. It is designed for high-speed data transmission and is capable of supporting 10 Gigabit Ethernet (10GbE) speeds over distances up to 100 meters (328 feet). Cat 7 cables are typically shielded, meaning they have an additional layer of protection to reduce electromagnetic interference (EMI) and crosstalk, which improves the signal quality and reliability of the network connection.
8 strands
Inner Jackets
Grounding Sheild

## Slide 11: CATEGORY 7A
Cat 7a (Category 7a) is an enhanced version of the Cat 7 cable, offering even higher performance. It is designed to support speeds up to 40 Gigabits per second (40Gbps) over shorter distances (up to 50 meters or about 164 feet) and can operate at frequencies up to 1,000 MHz, which is double the frequency of standard Cat 7 cables.
8 strands
Inner Jackets
Grounding Sheild (NET)

## Slide 12: CATEGORY 8.1
Cat 8.1 is a newer subcategory of Cat 8 cables that builds upon the original Cat 8 specification but offers some improvements in terms of performance and application.
8 strands
Inner Jackets
Grounding Sheild (NET)

## Slide 13: CATEGORY 8.2
Cat 8.2 is an advanced version of Cat 8 cable specifications, offering even higher performance compared to Cat 8.1, although both are relatively new in the category of Ethernet cables. The Cat 8.2 standard is a step forward in terms of high-speed capabilities, though it's not yet as commonly referenced or widely implemented as other Ethernet standards.
8 strands
Inner Jackets
Grounding Sheild (NET)

## Slide 14: CATEGORY 8.3
Cat 8.2 is an advanced version of Cat 8 cable specifications, offering even higher performance compared to Cat 8.1, although both are relatively new in the category of Ethernet cables. The Cat 8.2 standard is a step forward in terms of high-speed capabilities, though it's not yet as commonly referenced or widely implemented as other Ethernet standards.
8 strands
Inner Jackets
Grounding Sheild (NET)

## Slide 15: RJ-45 Connection
The eight-pin RJ45 connector is a standardised interface which often connects a computer to a Local Area Network (LAN)
8 Teeth Pins
Connection Clip
Connection Holder

## Slide 16: RJ-11 Connection
The registered jack 11 (RJ11) is a type of connector commonly used for telephone cables. It has four or six pins and is used to connect phones, modems, and other telecommunication devices to a wall jack or other phone line.
Connection Clip
Connection Holder
4 Teeth Pins

## Slide 17: Metal Vs Plastic
Ethernet connectors, often RJ45 connectors, can have either plastic or metal housings. Metal housings are more durable and offer protection against electromagnetic interference (EMI), making them ideal for shielded Ethernet cables in noisy environments. Plastic housings are more cost-effective and sufficient for unshielded cables in less demanding situations.
Grounded Clip
Non Grounded
Basic Cable Use
Stronger Case
Advanced Cable Use

## Slide 18: COLOR CODE
Each twisted pair of wires inside an Ethernet cable is color-coded to ensure they are connected to the appropriate pins on the RJ45 connector.

## Slide 19: T568A
T568A is the first of the two to be standardized and recognized.

## Slide 20: TRANSMITTING COLORS
What each wire inside oof Ethernet is used for.

## Slide 24: LINK LIGHT STATUS
What does each Ethernet link light indicate

## Slide 26: ETHERNET

## Slide 27
Press ESC to Exit